## Slide 1: Work on drone radiation detection
Urh Trinko

## Slide 2: 4.11.2022
Code for measurement of a specified area with a single radiation point source. This simulates flight of a drone over this area. The specifiable parameters are the properties of the source, the height of flight and size of the grid. The code places the point source randomly somewhere on the map. The intensities at certain positions are determined using the inverse square law.
The code for getting the position of the source from measurement data gathers the positions with similar intensities. This points are then fitted to a circle, the centre of which is the estimated position of the source.

## Slide 3
In this example only one set of intensities is used to make a circle and only one centre is calculated. Further improvement could be made by using more circles.

## Slide 4: 7.11.2022
Improvement of the point source location by using multiple different intensities to get multiple circle centres.
Some of them are then eliminated because they are to far, but the remaining (green points on right image) are averaged to get the estimation of the point source (black dot).
The right image only shows the tile with the largest intensity – “hotspot” tile.

## Slide 5: 8.11.2022
Improvement of the point source location-finding function. Previously all points outside of the tile with the largest intensity were eliminated. However there are examples in which no points exist inside the “hotspot” tile. This results in an error, because there are no points to average. This is fixed by gradually increasing the acceptable size of the area around the “hotspot” tile until at least one point is collected.

## Slide 6: 10.11.2022
Simulating entire code multiple times and collecting the distance betweenn the original random source and estimated one. Collecting this data and presentingng it in histogram form – Poisson distribution?
Also trying to calculate the standard distribution from least square method using sum of residuals, effective degrees of freedom and the covariance matrix (?) – PROBLEM: drastically different to the simulation standard deviation.

## Slide 7: 11.11.2022
Comparing the standard deviation for multiple random source positions through calculation and simulation. The simulation results are much less scattered then the calculated ones – possibly not correct yet, further work needed to really understand the covariance matrix.

## Slide 8: 14.11.2022
Comparing the relation between the uncertainty of the estimated source and the position of the original source on the grid. Compering the result between the simulated (left) and calculated (right) results.
Takeaway: We can see that for both images the deviations seem to be larger when the source is positioned at the edge of the grid. Makes sense because there is less data to gather.
Question: Why is the deviation larger on only one side on the left side?
In future: Modify the flight of the detector so it gets the data around the original source.

## Slide 9
Analysing the error in relation to the height of the fly-over, left – measured, right –calculated err.
At higher levels the error is less (?) but if you go too high the background shades everything.