## Slide 1: Work on drone radiation detection
Urh Trinko

## Slide 2: 4.11.2022
Code for measurement of a specified area with a single radiation point source. This simulates flight of a drone over this area. The specifiable parameters are the properties of the source, the height of flight and size of the grid. The code places the point source randomly somewhere on the map. The intensities at certain positions are determined using the inverse square law.
The code for getting the position of the source from measurement data gathers the positions with similar intensities. This points are then fitted to a circle, the centre of which is the estimated position of the source.

## Slide 3
In this example only one set of intensities is used to make a circle and only one centre is calculated. Further improvement could be made by using more circles.

## Slide 4: 7.11.2022
Improvement of the point source location by using multiple different intensities to get multiple circle centres.
Some of them are then eliminated because they are to far, but the remaining (green points on right image) are averaged to get the estimation of the point source (black dot).
The right image only shows the tile with the largest intensity – “hotspot” tile.

## Slide 5: 8.11.2022
Improvement of the point source location-finding function. Previously all points outside of the tile with the largest intensity were eliminated. However there are examples in which no points exist inside the “hotspot” tile. This results in an error, because there are no points to average. This is fixed by gradually increasing the acceptable size of the area around the “hotspot” tile until at least one point is collected.

## Slide 6: 10.11.2022
Simulating entire code multiple times and collecting the distance betweenn the original random source and estimated one. Collecting this data and presentingng it in histogram form – Poisson distribution?
Also trying to calculate the standard distribution from least square method using sum of residuals, effective degrees of freedom and the covariance matrix (?) – PROBLEM: drastically different to the simulation standard deviation.

## Slide 7: 11.11.2022
Comparing the standard deviation for multiple random source positions through calculation and simulation. The simulation results are much less scattered then the calculated ones – possibly not correct yet, further work needed to really understand the covariance matrix.

## Slide 8: 14.11.2022
Comparing the relation between the uncertainty of the estimated source and the position of the original source on the grid. Compering the result between the simulated (left) and calculated (right) results.
Takeaway: We can see that for both images the deviations seem to be larger when the source is positioned at the edge of the grid. Makes sense because there is less data to gather.
Question: Why is the deviation larger on only one side on the left side?
In future: Modify the flight of the detector so it gets the data around the original source.

## Slide 9
Analysing the error in relation to the height of the fly-over, left – measured, right –calculated err.
At higher levels the error is less (?) but if you go too high the background shades everything.

## Slide 10: 15.11.2022
Improving the location code by using the Levenberg-Marquardt (page 707) method for least square minimazition.
The model function is the inverse square law, where the adjustable parameters are u (x source coordinate), v (y source coordinate) and A0 (the activity of the source). We have a number of data points of intensities along the grid which gives us a overestimated system of equations.

## Slide 11: 16.11.2022
Successful in making the source locating code using the LM method in scipy. As we can se the accuracy is much higher then with the previous attempts.

## Slide 12: 17.11.2022
Implementing source location estimation with the scipy.optimize.curve_fit function, the upside of which is that we can input also the uncertainty of the dependant data.

## Slide 13: 18.11.2022
Testing the scipy curve_fit sigma absolute error so that it can later be used to specify the uncertainty of the detector for intensities.
FOR NEXT WEEK: Implement a detector constant and see how many measurements you have to make in order to get the same uncertainty for two different quality detectors.

## Slide 14: 21.11.2022
Adding the variable that contains standard deviation of the x, y coordinates and intensity. The code than adds some gaussian noise to the data. In the picture the sigmas are (0.5, 0.5, 100).
The scipy curve_fit is the point derived from the noisy data.

## Slide 15: 22.11.2022
In the code implementing factor K, which tells us the information on how many of the possible events we measured and also factor F, which tells us the ratio between the effective dose(for a specific radioactive element and inhalation or ingestion).
The relation F/(1-K) is the factor C, which tells us how good a detector is.
Code written so that this stands: effective_dose = C * activity; relative_error_effective_dose = 1 / \sqrt(effective_dose/C)

## Slide 16: 23.11.2022
Improving yesterdays code by changing effective_dose_error = 1/ \sqrt((effective_dose*T)/C), where T is the combined time of the flyover of the detector. So the longer we measure the more accurate the results will be. The equation yesterday also didn’t make sense unit wise also.
Comparing how many more grid points you need to get the same error of the effective dose for to different detectors.
Simulating the mentioned error for different girds and trying to find the relation between the two variables.

## Slide 17: 24.11.2022
CORRECTING code made from 22. and 23.11
Inside the loop pick a point, calculate the activity @ that point, multiply this activity with the number that takes into account detector quality.
Use this number multiplied by the time of measurement at that location as the expected value in a Poission distribution. Use the numpy.random.poisson command to determine the number of events measured by the detector at this location.
Get the measured dose speed by multiplying the number of events with the radioactive dose factor. Calculate the relative error of this by dividing one by the square root of the number of events.
Repat this also for the background radiation, by choosing a constant background expected value for the Poisson distribution.
Do this for each point and then fit the measured data to the inverse square law equation so that you get the searched parameters.

## Slide 18: 25.11.2022
Comparing the errors of x and y position of the estimated source (u, v parameters) to the different properties of the detector, detector factor K, height of flyover, number of grid points.
Checking if the results are what we expect for our simulation.

## Slide 19
Comments on the error analysis (previous slide).
Err(K): Error increases with K – logical because a larger K means an inferior detector. The error seems to increase faster as K becomes larger, similar to some kind of an exponential function. Weird thing happen when approaching 1 for K, that’s why the max value on the graph is 0.8. Further analysis here needed.
Err(h): The error increases with the height – logical because the background is not dependant on the height so it stays the same while the source signal decreases with 1/h**2. For smaller heights the error seems to increase as h**2 but for larger heights the increasing seems linear. EXCEPTION: sometimes for lower heights we get very big uncertainties.
Err(grid): The error decreased with more grid points – logical because this simply means more measurements were made. The decrease is very quick at first and then approaches 0 more slowly. This is reminiscent of the function 1/(n_grids). Err(dt) is similar.

## Slide 20: 29.11.2022
New flyover, where the detector choose random points in the grid where it measures the intensity
It seems that for smaller numbers of the difference between the errors for random and previously used method is the largest but for larger the numbers are similar (right image shows the the subtraction of the grid error from the random error – negative values therefore mean a lower grid error).

## Slide 21: 30.11.2022
Trying to fit a function with parameters to the graphs on day 25.11. So that we get some sort of table for how large an error would be for certain detector coefficient, height and number of grid points.
Starting to write an improved flyover for a single point source, where it will first locate the hotspot tile and then fly around that point while gathering information – number of events.

## Slide 22: 1.12.2022
Continue work on improved flyover.
Testing translation simetry by comparing the x and y errors for source in the middle and somewhere outside. We can see from the picture that there is no noticeable difference (y error larger then x).
MISTAKE!

## Slide 23: 5.12.2022
Simulating finding the source location 500 times for when the source is at the center of the coordinate system. The values deviate around x = 0 and form a gaussian curve. The deviation of this is similar to the one estimated by the code, so this seems to be working correctly.

## Slide 24: 6.12.2022
Comparisson between detector coefficient, height, number of grid points, time of measurement at each grid point and the relative error of the source location. Similar relations as for the ZIG-ZAG flyover (look on slide of 25.11.2022).
I noticed that the relations are much more scattered and you get results similar to the ZIG-ZAG flyover only when you have a lot of random measurements
Left image shows the relation for K to source position error for ZIG-ZAG flyover for 400 measurements. Middle one shows random flyover for 400 measurements and the right one for 1000.

## Slide 25
Also the error decreases the fastes with the increase of the number of grid tiles/points of measurement and the increase of the time spent measuring at each point.
Also note that the subsidiary code – simulate_event – didn’t work as intended.
And continue work on improved SPS.

## Slide 26: 7.12.2022
Completing the improved flyover code.
DESCRIPTION: We divide the area into tiles same as in the ZIG-ZAG. The detector starts at the top left tile. It measures the dose in the tile and comperes it to the neighbouring tiles (measures the right, diagonal and bottom tile to the first tile). If one of the tiles has a larger dose it moves there and continues the described measurement for it’s neighbours. The process is continued until the detector reaches the tile with the highest dose – hotspot tile. It then spirals outward around the centre of the hot spot tile.
PROBLEM: In some situation still questionable paths, but I think this is the result of the Poisson distribution which we use to simulate the measuring of the detector. This brings an uncertainty to the number of measured events. If we put in to many grid points and the source is to week the detector might stop before it reaches the hotspot. It checks the neighbour tiles and sees that non of them have a larger measured dose and so it stops.
FURTHER IMPROVEMENTS: Incorporate the error of the measurement into the movement of the detector.

## Slide 27
Visual path of the detector.

## Slide 28: 8.12.2022
Cleaning up the improve flyover code – adding the locatiocating of the source and compering the accuracy to the previous two methods (ZIG ZAG and RANDOM).
Checking if the dependency of the error to the detector constant, height... (check 25.11.2022) is consistent with the dependency from previous methods (some exeptions for time and grid – further analysis).

## Slide 29
MISTAKE NOTICED: On the 1.12.2022 I simulated a 2D color graph which showed the x and y error of the estimated source position. I claimed that there is no noticeable difference in the error of the points on the inner side of the grid and outer side of the grid. This is incorrect and was a result of an error code. In the loop where I should have set the parameter of the function to some source outside of the KS centre, I placed the KS centre every time.
The corrected code shows that the error is pretty constant inside of the grid but increases noticeably at the edges. This makes sense because if a source is generated near the edge it can only have measurements made on one side. This idea is supported by the comparison between the graphs for x and y errors. The increase in x error happens at the left end right edge, while for y errors at the top and bottom edge. This supports the idea because in each case there are less measured points for left/right (x error increase) and above/bellow of the source (y error increase).
Also there are no such edge increases for the spiral measurement, because measurements are always done around the source.

## Slide 30
Visual examples for the thought process on the previous slide – from top left: ZIG-ZAG, top right: RANDOM, bottom: SPIRAL.

## Slide 31: 9.12.2022
Simulating different methods (ZIG_ZAG, random and spiral) for random points at each grid tile and then displaying the estimated source error of the x-coordinate in a histogram (for every method)
For spiral an error occurs at the bottom left tile, origin yet UNKNOWN
We se that the error for the spiral method is generally lower (for all simulated methods the number of measurements made is THE SAME).

## Slide 32: 12.12.2022
Found a problem in spiral flyover – we get a IndexError and ValueError when the source is in the bottom right grid corner.
Also the source error position seems to become very high for some large time measurements.
I corrected the index and value errors. There was a unnecessary call for the make_list() function when the detector “was in” the last tile.
New problem -> with the correction above we now don’t get a uniform error distribution for the points on the grid (like on 8.12.2022), but rather there are two areas where the errors seem to always be grater (red circles).

## Slide 33
The change that fixed the problem for the bottom right tile source caused this problem. The error caused the while loop to continue going even after it reached the hotspot, stopping only when reaching the bottom right tile. So I fixed the code by adding another break in the while loop.
Now the errors seem to be pretty constant across the grid. There are some hotspots but seem to be random, because they change positions for different simulations. Bottom figures display errors for points on grid for different simulations, where in both cases all the parameters stayed the same. We can se that larger errors appear at different places (is this a sufficient explanation?)